## Slide 1
MOTORCYCLE EXPEDITION PLAN
Seattle → Deadhorse
The Dalton Highway to the Arctic Ocean
2002 BMW F650GS (base) · 5,845 mi · 27 days
Depart Sat Jun 26, 2027 · Home Thu Jul 22, 2027
TOTAL DISTANCE
5,845 mi
DALTON: JUL 8–12
414 mi
LONGEST FUEL GAP
239 mi
BUDGET
~$8,300

## Slide 2
THE FINDING THAT RESHAPED THIS TRIP
You cannot ride to Nome.
Nome has NO road connection to the North American highway system.
It is a fly-in / barge-in town. No highway reaches it from Fairbanks, Anchorage, or anywhere else.
Nome does have ~250–350 mi of its own gravel roads (Teller, Council, Kougarok) — but that
network is an island. It dead-ends into tundra and connects to nothing.
OPTIONS CONSIDERED
Fly the bike over
Air freight from Anchorage.
Real, but +$1.5–3k and 5–7 days.
Barge the bike
Cheap-ish, slow,
schedule-bound.
Winter overland
Done before. Expedition-grade.
Genuinely dangerous.
Deadhorse instead
Road-continuous.
The true end of the road.
DECISION: Deadhorse / Prudhoe Bay via the Dalton Highway. Nome parked as a possible future add-on.
2
Seattle → Deadhorse · 2002 BMW F650GS

## Slide 3
ROUTE
Seattle → BC → Yukon → Fairbanks → Deadhorse
Ride a LOOP: north one corridor, south the other. Same mileage, double the country.
NORTHBOUND — Stewart–Cassiar (BC-37)
~450 mi · Remote, quiet, fully paved.
More wildlife, fewer services.
Side trip to Stewart/Hyder is worth it.
SOUTHBOUND — Alaska Highway (Alcan)
1,387 mi Dawson Creek → Delta Junction.
More services, more traffic.
The historic route.
LEG DISTANCES (one way, via Cassiar — planning estimates)
Seattle → Prince George
800
Prince George → Kitwanga
450
Cassiar → Alaska Hwy jct
450
Watson Lake → Whitehorse
275
Whitehorse → Tok, AK
400
Tok → Fairbanks
200
Fairbanks → Deadhorse
500
SEATTLE → DEADHORSE
≈3,000
Round trip ≈ 6,000–6,500 mi. Budget 3–4 weeks at a sane pace.
3
Seattle → Deadhorse · 2002 BMW F650GS

## Slide 4
THE DALTON HIGHWAY
Everything south of Fairbanks is a normal trip. This isn't.
414 miles, Livengood → Deadhorse. Majority unpaved. No cell service.
TRUCKS OWN THE ROAD
Heavy oilfield traffic. Get over, slow down, expect flying rock.
Truck-thrown stone is the #1 source of damage.
CALCIUM CHLORIDE
Dry: packs hard, feels like pavement, lulls you.
WET: greasy 'peanut butter' — it WILL put you down.
Also corrosive — wash the bike immediately after.
ATIGUN PASS · 4,739 ft
Weather can be full winter in any month.
No services. No signal. No help.
PACING: 4 days from Fairbanks and back. Fairbanks → Coldfoot → Deadhorse → Coldfoot → Fairbanks
4
Seattle → Deadhorse · 2002 BMW F650GS

## Slide 5
CONSTRAINT #1
The fuel gap is longer than your range.
Fuel exists at exactly THREE places on the Dalton.
YUKON RIVER CAMP
MP 56
COLDFOOT
MP 175
DEADHORSE
MP 414
COLDFOOT → DEADHORSE
Longest fuel gap on ANY public road in the United States.
239 mi FUEL GAP
230 mi YOUR RANGE
F650GS: 4.4 gal · ~50 mpg · ~230 mi claimed. Derate for load, headwind, gravel, low gear → assume ~200 mi.
YOU WOULD RUN DRY BEFORE DEADHORSE.
And you can't fix it with a bigger tank — the F650GS tank is UNDER THE SEAT, inside the frame.
No long-range tank exists for this bike.
5
Seattle → Deadhorse · 2002 BMW F650GS

## Slide 6
CONSTRAINT #1 — SOLVED
Carry external fuel. It's a $100 problem.
CONFIGURATION
TOTAL RANGE
VERDICT
Stock tank only
~200–230 mi
NOT ENOUGH
+ 1 gal Rotopax
~280 mi
SOLVES IT
+ 2 gal Rotopax
~330 mi
COMFORTABLE
RECOMMENDATION
1–2 gal Rotopax on a rear rack, carried on the Dalton only. Leave it behind for the pavement miles.
DISCIPLINE: Top off at Yukon River (MP 56) and Coldfoot (MP 175) EVERY time, without exception.
There is no “I'll get it at the next one.”
6
Seattle → Deadhorse · 2002 BMW F650GS

## Slide 7
THE MACHINE
2002 BMW F650GS — base model
SPECS
Engine
652cc single (Rotax)
Wheels
19" front / 17" rear
Tire sizes
110/80-19 · 140/80-17
Fuel
4.4 gal — UNDER THE SEAT
Weight
~430 lb wet
VERDICT: A GOOD CHOICE
Proven round-the-world bike. Comfortable over the
2,400 pavement miles north. Light enough to pick
up alone — which you WILL need to do.
This is not a compromise pick.
BASE, NOT DAKAR
19" front + shorter travel = modest disadvantage.
Not a problem — just ride slower.
MECHANICAL REFRESH — DONE ✓
Completed before July 2026. Retires the single
biggest risk in the plan.
⚠ THE BIKE IS 24 YEARS OLD — RELIABILITY IS A SAFETY ITEM, NOT A MAINTENANCE ITEM
A breakdown on the Dalton is an emergency: no cell service, 240 mi between services, and a tow costs more than the bike.
7
Seattle → Deadhorse · 2002 BMW F650GS

## Slide 8
KNOWN F650GS FAILURE POINTS
Address every one of these before departure.
FUEL PUMP + CONTROLLER
Known failure on this generation. In-tank, under the seat.
Fails on the Dalton = trip over, in the worst possible place.
CARRY A SPARE
FUEL-LEVEL “STRIP” SENSOR
Famously fails. Normally a shrug — ride by trip meter.
But your range is ALREADY short of the 239 mi gap.
FIX IT
WATER PUMP SEAL
Classic wear item. Check the weep hole for coolant.
INSPECT
STATOR / REG-RECTIFIER
Check charging voltage.
INSPECT
VALVE CLEARANCES
Check and set.
INSPECT
8
Seattle → Deadhorse · 2002 BMW F650GS

## Slide 9
TIRES
Don't optimize for the 8% of the trip that's dirt.
Round trip ≈ 6,000 mi. The Dalton is ~600 mi of it. A soft knobby rear can be cooked in ~3,000 mi —
you would destroy it just GETTING to Fairbanks.
HEIDENAU K60 SCOUT
Comes in 140/80-17. Riders report
10,000+ mi on a set. Adequate on the
Dalton, excellent everywhere else.
One set does the whole trip.
Downside: hard to mount.
RECOMMENDED
CONTINENTAL TKC80
Better in mud, but wears fast — and
Continental is PHASING IT OUT.
Replaced by the redesigned TKC80²
(small sizes May '26, large Aug '26).
If you go Conti, go Gen 2.
GEN-2 ONLY
MITAS E-07
More like 60/40 street.
Long-wearing.
Fine — but the K60 does the same
job with more dirt capability.
REDUNDANT
RECOMMENDATION: Heidenau K60 Scout front + rear. One fresh set, whole trip.
No mid-trip swap, no shipping tires to Alaska.
⚠ VERIFY EARLY: the 140/80-17 rear is an oddball size with few options. If it dries up, this changes.
9
Seattle → Deadhorse · 2002 BMW F650GS

## Slide 10
THE DESTINATION
Deadhorse is an industrial camp, not a town.
No beach. No bar. No triumphant sign worth much. Manage expectations — the ride is the reward.
LODGING — book ahead, they sell out
• Aurora Hotel
• Prudhoe Bay Hotel
• Deadhorse Camp
Rustic, camp-style. Meals usually included.
YOU CANNOT RIDE TO THE ARCTIC OCEAN
The final stretch crosses secured oilfield
property. You must take an ESCORTED SHUTTLE.
Book in advance (24h min for the security
check). Bring government photo ID.
Camping in Deadhorse is effectively not a thing. Budget for a room.
SEASON & TIMING
WINDOW
mid-June → early Sept
PEAK
late June / July
BUGS
brutal in Jun–Jul
TRIP LENGTH
3–4 weeks
10
Seattle → Deadhorse · 2002 BMW F650GS

## Slide 11
GEAR, SAFETY & BORDER
The non-negotiables
SAFETY — NON-NEGOTIABLE
• Satellite communicator (inReach / ZOLEO).
No cell on the Dalton — your ONLY way to
call for help.
• Bear spray — accessible, not in a pannier
• Ability to fix a flat (tubes, irons, pump)
• First aid + a day of food & water
GEAR
• Layers rated for near-freezing + rain
• Heated grips / vest — worth it
• Real rain gear. You WILL ride in rain.
• Head net + DEET (mosquitoes are real)
• Camping kit rated below expected lows
BORDER — YOU CROSS INTO CANADA TWICE
• Passport (not just a passport card)
• Proof of insurance VALID IN CANADA — US policies are not automatically valid. Confirm with your insurer.
• Vehicle registration · Cash in CAD + USD (remote stops can be card-flaky)
FIREARMS: DO NOT. A handgun in Canada is a serious offense and ends the trip at the border. Bear spray is the answer.
11
Seattle → Deadhorse · 2002 BMW F650GS

## Slide 12
SEASON — LOCKED
Depart Saturday, June 26, 2027.
Chosen so the Dalton run lands July 8–12 — dead center of the peak window.
DEPART
Sat Jun 26
DALTON
Jul 8 – 12
HOME
Thu Jul 22
DURATION
27 days
WHAT THIS BUYS YOU
Warmest temps · Atigun Pass clear of snow · near-24-hour daylight — and the best odds of a DRY
Dalton. Dry, the calcium chloride packs hard and grips. Wet, it's the thing most likely to put you down.
THE TRADEOFF
Peak mosquito season. A nuisance, not a hazard.
The head net is not optional.
IF IT SLIPS
Slip it in WHOLE WEEKS. Do not let it drift
toward September — the Dalton turns.
SHAPE OF THE TRIP
10 days north (Cassiar) → 5 days on the Dalton → 9 days home (Alcan). No day over 340 mi.
12
Seattle → Deadhorse · 2002 BMW F650GS

## Slide 13
DAY BY DAY · ★ = OFF DAY (5 TOTAL — LOAD-BEARING, NOT LUXURY)
27 days · 5,845 miles · 266 mi average riding day
1
Jun 26
Seattle → Hope, BC
185
2
Jun 27
Hope → Quesnel
330
3
Jun 28
Quesnel → Smithers
300
4
Jun 29
Smithers → Stewart
250
5
Jun 30
★ STEWART / HYDER — bears
—
6
Jul 1
Stewart → Dease Lake
270
7
Jul 2
Dease Lake → Watson Lake
250
8
Jul 3
Watson Lake → Whitehorse
275
9
Jul 4
★ WHITEHORSE — servicing
—
10
Jul 5
Whitehorse → Beaver Creek
290
11
Jul 6
Beaver Creek → Fairbanks
310
12
Jul 7
★ FAIRBANKS — Dalton prep
—
13
Jul 8
Fairbanks → Coldfoot
260
14
Jul 9
COLDFOOT → DEADHORSE
240
15
Jul 10
★ DEADHORSE — ARCTIC OCEAN
—
16
Jul 11
Deadhorse → Coldfoot
240
17
Jul 12
Coldfoot → Fairbanks
260
18
Jul 13
★ FAIRBANKS — wash the bike
—
19
Jul 14
Fairbanks → Tok
200
20
Jul 15
Tok → Destruction Bay
280
21
Jul 16
Destruction Bay → Whitehorse
160
22
Jul 17
Whitehorse → Watson Lake
275
23
Jul 18
Watson Lake → Fort Nelson
325
24
Jul 19
Fort Nelson → Dawson Creek
280
25
Jul 20
Dawson Creek → Prince George
250
26
Jul 21
Prince George → Cache Creek
275
27
Jul 22
Cache Creek → SEATTLE
340
13
Seattle → Deadhorse · 2002 BMW F650GS

## Slide 14
BUDGET
≈ $8,300 all-in.
ON-ROAD (27 days)
Fuel — 117 gal @ ~$5.25
$614
Lodging — Coldfoot ×2
$500
Lodging — Deadhorse ×2
$510
Lodging — Fairbanks ×4
$560
Lodging — other hotels ×7
$910
Camping ×11
$275
Food — ~$50/day
$1,350
Arctic Ocean shuttle
$89
Misc — wash, laundry, sundries
$150
SUBTOTAL
$4,958
PREP & GEAR (one-time)
Heidenau K60 Scout set + mount
$380
Rotopax 2 gal + rack
$150
Spare fuel pump + controller
$350
Chain + sprockets
$200
Tubes, filters, oil, consumables
$250
Protection (if not fitted)
$500
inReach + 2 mo (if not owned)
$450
SUBTOTAL
$2,280
TOTAL (incl. 15% contingency)
≈ $8,300
Gear already owned → ~$7,200. On-road only → ~$5,700 (about $184/day).
Soft spots: 2027 fuel price is a guess; Coldfoot's rate is UNVERIFIED — call (907) 474-3500.
14
Seattle → Deadhorse · 2002 BMW F650GS

## Slide 15
WHAT TO BOOK, AND WHEN
The Dalton has almost no beds.
Coldfoot and Deadhorse are the scarcest things in the plan. Everything else can be improvised.
NOW → JAN 2027
Coldfoot × 2 nights (Jul 8, Jul 11)
SCARCEST BED IN THE PLAN
NOW → JAN 2027
Deadhorse × 2 nights (Jul 9, Jul 10)
BOOK ~A YEAR OUT
~APR 2027
Fairbanks × 4 (Jul 6, 7, 12, 13)
~APR 2027
Whitehorse × 2 · Stewart × 2
~JUN 2027
Arctic Ocean shuttle
24h min — but book weeks out
ROLLING
Everything else — BC/Yukon camps are first-come
Deadhorse confirmed: Prudhoe Bay Hotel $260 · Deadhorse Camp ~$249 · shuttle $89/person.
15
Seattle → Deadhorse · 2002 BMW F650GS

## Slide 16
WHERE WE ARE
Resolved vs. open
RESOLVED
✓ SEASON: summer 2027 — Jun 26 → Jul 22
✓ Itinerary + budget built (27 days)
✓ Destination: Deadhorse, not Nome
✓ Bike: 2002 F650GS, base (19"/17")
✓ Mechanical refresh complete
✓ Fuel: 1–2 gal Rotopax
✓ Carry spare fuel pump + controller
✓ Tires: Heidenau K60 Scout, one set
✓ Route: Cassiar north, Alcan south
OPEN
BOOK COLDFOOT + DEADHORSE.
Scarcest beds in the plan — book
~a year out. This is now urgent.
Confirm K60 Scout in 140/80-17 —
the whole tire plan rests on it.
Did the refresh cover the strip sensor,
water pump seal, stator, valves?
Solo, or with others?
Shakedown ride — spring 2027
NEXT STEPS
1. BOOK Coldfoot ×2 + Deadhorse ×2 → 2. Confirm K60 in 140/80-17 → 3. Fit Rotopax + rack
4. Shakedown ride, loaded, on gravel → 5. Confirm insurance is valid in Canada
16
Seattle → Deadhorse · 2002 BMW F650GS